## Slide 1: Machine Learning based Intrusion Detection System for Cyber Physical Power System
Thesis Defense
Date:

## Slide 2: By Abdul Wahab 19132
Supervised By Dr. Muhammad Zubair designation

## Slide 3: Introduction
Smart grids – are a combination of IT with traditional grid and thereby offers stronger control over the functions
  Across the world, governments are urging grid operators to utilize the latest technologies
  Resilience to cyber attacks is important for faster adoption of future automated electrical power system
  Cyber adversary can manipulate data (Sensor readings, synchronization signals etc.) and commands (feedback control signals) exchanged by conducting camouflaged logical or physical attacks
Notes: Pan, Shengyi, Thomas Morris, and Uttam Adhikari. "Developing a hybrid intrusion detection system using data mining for power systems." IEEE Transactions on Smart Grid 6, no. 6 (2015): 3104-3113.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.
“Kitsune: An Ensemble of Autoencoders for Online Network Intrusion Detection” NDSS ’18, 18-21 February 2018, San Diego, CA, USA

## Slide 4: Problem Statement
Development of an IDS for Cyber physical electrical power transmission system with following capabilities,
  Unsupervised Learning
  Online classification
  Better zero day detection
  Ability to run on commodity device (Raspberry Pi)
Notes: Pan, Shengyi, Thomas Morris, and Uttam Adhikari. "Developing a hybrid intrusion detection system using data mining for power systems." IEEE Transactions on Smart Grid 6, no. 6 (2015): 3104-3113.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.
“Kitsune: An Ensemble of Autoencoders for Online Network Intrusion Detection” NDSS ’18, 18-21 February 2018, San Diego, CA, USA

## Slide 5: Problem Statement
Research objectives
  “Design a lightweight*, plug-and-play anomaly based CP-IDS, to embed directly in an Intelligent electronic device (IED), capable of learning in unsupervised manner”
  “Develop a stream processing algorithm for online classification of high-speed WAMS (Wide area monitoring system) data”
  “Establish the possibility of applying gaussian theories and correntropy approaches to model the multi-variate data of synchro-phasor based WAMS of cyber physical power transmission systems”
  * (Learning and execution algorithms with very low computing and memory footprint)
Notes: Pan, Shengyi, Thomas Morris, and Uttam Adhikari. "Developing a hybrid intrusion detection system using data mining for power systems." IEEE Transactions on Smart Grid 6, no. 6 (2015): 3104-3113.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.
“Kitsune: An Ensemble of Autoencoders for Online Network Intrusion Detection” NDSS ’18, 18-21 February 2018, San Diego, CA, USA

## Slide 6: Significance of work
Improved intrusion detection and resilience to cyber attacks is essential for faster adoption of smart grids and future automated electrical power system.

## Slide 7: Potential Benefit
This research work contributed to the field of electrical, industrial informatics, machine learning and data science by,
  Developing a novel stream processing algorithm for state of the art synchrophasor based WAMS high speed data
  Establish the possibility of applying Gaussian theories to the electrical quantities of the smart grid.

## Slide 8: Related Work / Literature Survey
Adhikari, Uttam (Aug. 2015). “Event and intrusion detection systems for cyber-physical power systems”. PhD thesis, Department of Electrical and Computer Engineering, Mississippi State University.
Haider, Waqas (Dec. 2018). “Developing Reliable Anomaly Detection System for Critical Hosts: A proactive Defense Paradigm”. PhD thesis. School of Engineering and Information Technology, The University of New South Wales.
Mirsky, Yisroel et al. (2018). “Kitsune: an ensemble of autoencoders for online network intrusion detection”. In: arXiv preprint arXiv:1802.09089.
Reference 1, helped in in-depth understanding of ORNL (Oak Ridge National Lab) power transmission system datasets and acquaintance of pioneer work in power transmission subsystem event and intrusion detection domain
From Reference 2, utilized the concepts to design the probability based decision engine, while Reference 3, helped in design principals for online decision engine.

## Slide 9: Limitations of Existing Techniques
Limitations - Existing EIDS
  Offline learning and Laborious process of supervised learning
    Collect measurements and logs
    Label measurements and logs
    Train machine learning model on labeled data
    Deploy the trained model to the device
    Execute the model on observed measurements
  High processing cost
  Low accuracy

## Slide 10: Challenges
Destructive-stealthy patterns Data collection and communication in power transmission control systems are subjected to contaminate with stealthy-data pattern
  Attacker – monitor normal system and mix up payload to camouflage abnormal behavior
  High similarity b/w natural events and malicious-intentional physical faults
  High similarity b/w legitimate and illegal command and control artifacts

## Slide 11: Challenges
Variety, Velocity and volume (3Vs)
  A dataframe of size [120 x 28] per pmu in a second
Validity - Challenges and Limitations
  Using literature, analytical and empirical analysis by considering prevalent ML Algorithms and available power system dataset of ORNL and Mississippi State University

## Slide 12: Flare overview
A flare, is a type of firework that produces a brilliant light and is used for signaling, illumination, or defensive countermeasures in civilian and military.
So too, Flare is a lightweight EIDS, capable of signaling the anomalies, to take defensive countermeasures.

## Slide 13: Flare overview
Relay
Phasor measurement unit
28 x Measurements
Current
Voltage
Magnitude
Impedance
Frequency
snort
Snort Log
TRUE
FALSE
Relay Status
TRUE
FALSE
control room
Control Room SW Log
TRUE
FALSE
Alert

## Slide 14: Feature Engineering
Quantity / Phase | Phase1 | Phase 2 | Phase 3
Voltage Phase Angle | PA1:VH | PA2:VH | PA3:VH
Voltage Magnitude | PM1:V | PM2:V | PM3:V
Current Phase Angle | PA4:IH | PA5:IH | PA6:IH
Current Magnitude | PM4:I | PM5:I | PM6:I
Zero Voltage Phase Angle | PA7:VH | PA8:VH | PA9:VH
Zero Voltage Magnitude | PM7:V | PM8:V | PM9:V
Zero Current Phase Angle | PA10:IH | PA11:IH | PA12:IH
Zero Current Magnitude | PM10:I | PM11:I | PM12:I
Quantity | Symbol
Frequency | F
Frequency Delta | DF
Apparent Impedance | PA:Z
Apparent Impedance Angle | PA:ZH
Status Flag | S
Control Panel Log | C
Snort | SN
Relay Log | RL
+
8+24=32
How the best features selection
Used domain knowledge
Statistical
Exploratory data analysis (EDA) i.e plotting etc.
Weka ml platform
  Pearson’s correlation coefficient
  Information gain (also called entropy)
Quantity / Phase | Phase1 | Phase 2 | Phase 3
Voltage Magnitude | PM1:V | PM2:V | PM3:V
Current Magnitude | PM4:I | PM5:I | PM6:I
Zero Voltage Magnitude | PM7:V | PM8:V | PM9:V
Zero Current Magnitude | PM10:I | PM11:I | PM12:I

## Slide 15: Flare overview
Alert
Flare
Flare can be deployed at:
  Substation – A Dedicated server or SBC
  Central Control Center – A Dedicated Server
next()*, a python object iterator, is used to simulate the real world power transmission WAMS using ONRL datasets.
* An iterator is an object which implements the iterator protocol, return the next item from the container (i.e. a csv file)

## Slide 16
Gaussian mixture model (GMM) and Correntropy
  Promising results by GMM and Correntropy approaches reported in literature [1], [2], [3], [4] and [5]
    Their use in the Electrical Power system event and intrusion detection domain is novel.
  GMM allows us to aggregate a multivariate data sequences of power transmission control system into one variable to have numeric behavioral representation for decision making
  Correntropy measure is operated on the posterior probabilities of the GMM to accurately establish the baseline for the normal system and detect anomalies.
Flare overview

## Slide 17
  How and why GMM and Correntropy (Corr-GMM) is used
  Considering the measurements from the power transmission system as continuous random variables (r.v.), malicious-stealthy-data patterns and legitimate event data dynamics can be viewed as errors.
  These errors can play a vital role from decision engine point of view
  Errors create an element of bias in data sequences
  To process non-Gaussian and impulsive noises the notion of Correntropy, which is a local measure of the similarity between any two random variables, is suggested in [Haider, PHD Thesis]
Flare overview

## Slide 18: Centrality – Gaussian distribution
*Plots created in Minitab V18
  Central Limit Theorem (CLT) - Histograms of sampling means of power system WAMS’s 28 x quantities, voltage and current synchro-phasors tends to be normally distributed / gaussian, can be visualized in the plots below

## Slide 19: Power Line faults and contingencies
Power Line Faults

## Slide 20: Power Line faults and contingencies
Line Maintenance

## Slide 21: Cyber Attack on Power System
Data Injection Attack

## Slide 22: Cyber Attack on Power System
Command Attack

## Slide 23: Decision Engine (DE)
Synchrophasor measurements
Data Logs from,
  Snort
  Control panel
  Relays
Gaussain Probability
density
estimation
Event Parsor
And
Processer
1
1
2
2
3
CorrEntroy
3
4
CorrEntroy
Detector Threshold
4

## Slide 24: Decision Engine (DE) cont.
  How and why GMM and Correntropy (Corr-GMM) is used
  We utilized the posterior probabilities of the data sequences obtained from GMM as input to the Correntropy as suggested in [Haider, PHD Thesis] Because the interdependency of the power system’s data sequences can be more reliably estimated based on their prior and likelihood data distributions
  Correntropy measure is used to create the precise behavioral boundaries for classification purposes.
  How achieved low memory and computation complexity and made it deployment ready
  During execution, once model executed with an instance [120 x 8], the instance is immediately discarded

## Slide 25: How Flare works
Symbol | Description
 | A multi-dimensional random variable, ; where m is the number of features
 | Feature variable;
 | Mean of observations of jth feature
 | Standard Deviation of observations of jth feature
 | Probabilistic proportions/ weight of each feature
and | 3.14159 and 2.71828
 | Gaussian/ Normal Distribution
Symbol | Description
 | Mean of observations of jth feature
 | Standard Deviation of observations of jth feature
 | Probabilistic proportions/ weight of each feature
 | 3.14159 and 2.71828
 | Gaussian/ Normal Distribution
important notations to proceed in-depth understanding of Flare working mechanism

## Slide 26: How Flare works
π = 3.14159
e = 2.71828
I = {xi1,…xij,…xim}
Each feature variable (i.e. PMU’s quantities) comprise n measurements, where the ith reading from the m-dimensional X variable space is expressed as,
Each feature variable can be modeled gaussian distribution (GD) and probability density function is estimated
Eq 1

## Slide 27: How Flare works
The posterior probability of taking the ith measurement value (Xi)
formulated by,
The posterior probabilities of all the whole measurements can be
estimated by,
Eq 2
Eq 3

## Slide 28: How Flare works
The Correntropy of the two consecutive observations,
| )
Correntropy-induced metric (CIM) employed by (Haider, 2018) to measure the local similarity between to measurements, for any two observations (A and B) is as:
Upper and Lower correntropy values are used to accurately specify a normal proﬁle,
Eq 4
Eq 5
Eq 6

## Slide 29: Flare - Learning
Input
i for sequences and k for features) | k=1 | k=2 | k=3 | k=4 | Label
i=1 | 1 | 2 | 3 | 4 | Normal
i=2 | 2 | 3 | 4 | 5 | Normal
i=3 | 3 | 4 | 5 | 6 | Normal
i=4 | 4 | 5 | 6 | 7 | Normal
i=5 | 5 | 6 | 7 | 8 | Normal
i=6 | 6 | 7 | 8 | 9 | Normal
Mean (µ) | 3.5 | 4.5 | 5.5 | 6.5
Standard deviation (σ) | 1.870828693 | 1.870828693 | 1.870828693 | 1.8708286
Variance ( ) | 3.5 | 3.5 | 3.5 | 3.5
Weight (𝜔) | 0.25 | 0.25 | 0.25 | 0.25
Parameters Estimation

## Slide 30: Flare - Learning
Probability Density Function (PDF) estimation
0.087319877 | 0.087319877 | 0.087319877 | 0.087319877
0.154625597 | 0.154625597 | 0.154625597 | 0.154625597
0.205762168 | 0.205762168 | 0.205762168 | 0.205762168
0.205762168 | 0.205762168 | 0.205762168 | 0.205762168
0.154625597 | 0.154625597 | 0.154625597 | 0.154625597
0.058951848 | 0.120422536 | 0.18485618 | 0.213243619
0.021829969 | 0.021829969 | 0.021829969 | 0.021829969
0.038656399 | 0.038656399 | 0.038656399 | 0.038656399
0.051440542 | 0.051440542 | 0.051440542 | 0.051440542
0.051440542 | 0.051440542 | 0.051440542 | 0.051440542
0.038656399 | 0.038656399 | 0.038656399 | 0.038656399
0.014737962 | 0.030105634 | 0.046214045 | 0.053310905
PDF with weights
0.087319877
0.154625597
0.205762168
0.205762168
0.154625597
0.144368546
Posterior
-eq 1
-eq 2
-eq 3

## Slide 31: Flare - Learning
Calculate correntropies
Calculate the upper correntropy and lower correntropy using
equation 5 and 6.
-eq 4
1.000007444
1.000008769
1.000008944
1.000007444
1.000005945
1.000007195
Lower corr normal | 1.000005945
Upper corr normal | 1.000008944

## Slide 32: Flare – During execution
Estimate the PDFs using the parameters of normal profile and
Calculate the correntropies using equations mentioned before.
Compare the correntropies against the decision correntropies
using,
After the executing the model with an instance, the instance is immediately discarded.

## Slide 33: results
  Flare Performance Evaluation
    To evaluate the performance of Flare, we performed benchmarks,
      On a Raspberry Pi 3 Model B, 1.2 GHz and 1GB RAM (Substation Depl)
      A Windows 10 running on an Intel Core i7 CPU 870, 2.93 GHz with 8GM (Central Depl)
    Complete implementation is done in Python.
The DR, FAR represents the accurac and error of Flare, respectively. The
FAR is the average of two errors, the False Positive Rate (FPR) and False
Negative Rate (FNR).
FAR can well indicate the capacity of Flare to incorrectly detect normal behavior as abnormal and abnormal behavior as normal, respectively (Haider, 2018).

## Slide 34: datasets for Cen Depl
Attacks Name | Description | # of measurements | Train [sec] | Execute [sec]
Data Injection | Imitation of a valid fault by changing values to parameters such as current, voltage, sequence components etc. This attack aims to blind the operator and causes a black out. | Train = 2423 Execute = 11564 | 22 | 100
Command injection - Remote trip relay | Attacker sends a command to a relay which causes a breaker to open. It can only be done once an attacker has penetrated outside defenses | Train = 2423 Execute = 10719 | 21 | 93
Event Name | Description | # of measurements | Train [sec] | Execute [sec]
Short-circuit fault | This is a short in a power line and can occur in various locations along the line. | Train = 2423 Execute = 16982 | 21 | 93
Line Maintenance | Relays is disabled on a specific line to do maintenance for that line | Train = 2423 Execute = 5291 | 22 | 46

## Slide 35: datasets for Cen Depl
Scenario | Description | # of measurements | Train [sec] | Execute [sec]
Command injection - Relay setting change | Relays are configured with a distance protection scheme and the attacker changes the setting to disable the relay function such that relay will not trip for a valid fault or a valid command. | Train = 2423 Execute = 39326 | 21 | 364
Anomaly | The training dataset is composed o f the measurements from normal, natural faults and line maintenance and test dataset composed of | Train = 12490 Execute = 65889 | 115 | 639

## Slide 36: datasets for Substation Depl
Scenario | # of measurements | Train [sec] | Execute [sec]
Short-circuit fault | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 14243 | 43 | 137
Line Maintenance | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 3041 | 43 | 127
Data Injection | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 9582 | 43 | 192
Command injection - Remote trip relay | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 8739 | 43 | 44
Command injection - Relay setting change | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 36159 | 43 | 142

## Slide 37: results – Central Deployment
Scenario | FPrate | FNrate | Error Rate | DRate
Attack vs. Normal | 3.0328 | 4.603 | 3.818 | 95.39745835
Data Injection vs. Normal | 7.8204 | 0.714 | 4.267 | 99.28634168
Line Maintenance vs. Normal | 7.8204 | 1.398 | 4.609 | 98.60228717
Fault Events vs. Normal | 7.8204 | 0.714 | 4.267 | 99.2857643
Command Injection vs. Norma | 7.8204 | 2.291 | 5.056 | 97.7092828
Relay Setting Change vs. Normal | 7.8204 | 4.909 | 6.365 | 95.09097435

## Slide 38: results – Substation Deployment
Scenario | FPrate | Fnrate | Errorrate | Drate
Command Injection | 0 | 1.513877208 | 0.75694 | 98.486
Data Injection | 9.2 | 4.6 | 0.75694 | 90.79
SLG Fault | 0 | 3.25 | 1.62 | 96.74
Line Maint | 0 | 3.25 | 1.62 | 96.74
Relay Setting Change | 0 | 9.2 | 4.6 | 90.72

## Slide 39: Comparison
  Most of the work in literature is focused on improvement of decision engine’s detection capability rather than deployment concerns, which was the pivot point of our research.
  Comparison is not an easy task as common ground is needed for true comparison, however an effort is made to compare the detection accuracy of algorithms for ORNL power system datasets against the proposed system.
  Flare’s results reported are obtained using raspberry PI, as the training and testing algorithms were designed with the purpose of low computing and memory footprints

## Slide 40: Comparison with other ml lgos
Chart: 
| Non mested generalized Exampler (NNGE) | JRipper+Adaboost | Sequential Pattern Mining algorithm | Temporal state-based specifications Learning | Fuzzy c-means (FCM) algorithm combined with the fuzzy inference system (FIS) | Specification-Based and Decision trees, instance-based learning and NNGE | Extreme Learning Machine (ELM) model optimized by the Adaptive Elitist Differential Evolution algorithm (AEDE) | Stacked Autoencoders | Flare (Proposed Decision Engine)
Accuracy ( % age) | 94 | 95 | 93.21 | 90.4 | 99.11 | 96 | 96.55 | 98.94 | 94.69
Chart: 
| MultiLayer Perceptron | Naïve Bayes | Iterative Dichotomiser 3 | Random Forest | Jrip | Sequential minimal optimization | Flare (Proposed Decision Engine)
Correctly Classified (% age) | 70.63 | 63.91 | 74.72 | 100 | 73.78 | 71.21 | 94.69
Results obtained by using WEKA
Results reported in literature

## Slide 41: Limitation of the proposed system
  At its current development stage, the main limitations of the Flare decision engine, training and execution algorithms are,
    Flare’s assumption that all measurements of WAMS are benign during train-mode
    “During training, an attack already in its execution phase will cause the DE to train on malign measurements, which will badly impact its decision capabilities. This risk can be minimized by ensuing the system is not under attack when the Flare is deployed.”
    The dataset used for evaluation of the Flare, is generated using a power transmission
    “Reported results and performance capability of Flare may change in real world deployment”
    Flare is not immune to adversarial machine learning
    “ Advance adversary can craft malicious inputs to mislead the Flare’s core algorithm model (Kurakin, Goodfellow, and Bengio, 2016)”

## Slide 42: Open research questions
  How the risk of ill-learning can be minimized in case of an attack already in execution phase during training?
  Develop the capability of Flare to counter the adverbial machine learning.
  How the accuracy of the developed Gaussian Mixture Modeling based DE can be improved?
  What are the best features of power systems for online classiﬁcation?
  Evaluate the Flare’s performance capability in real-world production power transmission system.

## Slide 43: Literature
Algorithm(s) | Result
Naïve Bayes,OneR, NNge, Jripper,Random Forests,SVM,Adaboost | JRipper+Adaboost having the highest overall F-Measure 0.955
Novel Specification-based Bayesian network | 100% for Nine scenarios
Sequential Pattern Mining algorithm | 95 % for Experiment 1 87.6% fro Experiment 2 93.21 % for Experiment 3
Temporal state-based specifications Learning | 90.4 % accuracy 73.43 % For Zero-days
Fuzzy c-means (FCM) algorithm combined with the fuzzy inference system (FIS) | 99.11 % Overall accuracy
Hoeffding Adaptive Trees (HAT) augmented with the drift detection method (DDM) and adaptive windowing (ADWIN) | The average kappa statistic was 94% for binary and 93% for multiclass classification.
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 44: Literature
Algorithm(s) | Result
Specification-Based and Decision trees, instance-based learning and NNGE | NNGE+STEM algorithm provides 96% and 93% detection accuracy for Binary and Multi Class datasets HAT algorithm provides 98% and 92% for Binary and Multi Class datasets respectively
Non mested generalized Exampler (NNGE) with State Extraction Method (STEM) | 94.0% with NNGE for Multiclass Classification 98% with NNGE for Binary Class Classification 99.54% with NNGE for Multi Class Classification on the IEEE 9 Bus System
Extreme Learning Machine (ELM) model optimized by the Adaptive Elitist Differential Evolution algorithm (AEDE) | 96.55% with proposed AEDE-ELM
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 45: Literature
Algorithm(s) | Result
Stacked Sutoencoders | 99.89 % for Normal Events 98.94 % for Data Injection Attacks 97.34% for Command Injection Attack 98.53 % for Relay Setting Change Attack
Probabilistic classification (Bayesnet), Rule induction (OneR, Ripper), Decision tree learning (C4.5), Non-probabilistic binary classification (SVM), The Ensemble Methods (Adaptive boosting, Bagging, Majority voting, Random forest) | Bagging C4.5, Adaboost Ripper, Adaboost C4.5 and Random forest achieved more than 90 % accuracy
NNGE HAT Common Path Mining | 94 % with NNGE 94% with HAT 93% with Common Path Minng Algoithm
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 46: End …
Any Question