## Slide 1: “A light weight event and intrusion detection system for cyber physical electrical power system” Abdul Wahab
Flare

## Slide 2
INTRODUCTION
RESEARCH MOTIVATION
FLARE OVERVIEW
POWER SYSTEM FAUTLS, CONTIGENCIES AND ATTACKS
FLARE SYSTEM DESIGN
RESULTS
  Existing detectors accuracy and error while detecting zero day attacks using tommy moris data
Outline

## Slide 3
Smart grids – are a combination of IT with traditional grid and thereby offers stronger control over the functions
  Across the world, governments are urging grid operators to utilize the latest technologies
  Resilience to cyber attacks is important for faster adoption of future automated electrical power system
  Cyber adversary can manipulate data (Sensor readings, synchronization signals etc.) and commands (feedback control signals) exchanged by conducting camouflaged logical or physical attacks
Introduction

## Slide 4
Research objectives
  “Design a lightweight*, plug-and-play anomaly based CP-IDS, to embed directly in an Intelligent electronic device (IED), capable of learning in unsupervised manner”
  “Develop a stream processing algorithm to classify high-speed data of WAMS (Wide area monitoring system)”
  “Establish the possibility of applying gaussian theories and correntropy approaches to model the multi-variate data of synchro-phasor based WAMS of cyber physical power transmission systems”
  * (Learning and execution algorithms with very low computing and memory footprint)
Introduction cont.
Notes: Waqas Haider, PHD research work “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, 2018, The University of New South Wales
A. Lagrange, M. Fauvel, and M. Grizonnet, “Large-scale feature selection with gaussian mixture models for the classification of high dimensional remote sensing images,” IEEE Transactions on Computational Imaging, vol. 3, no. 2, pp. 230–242, 2017.
L. P. Queiroz, F. C. M. Rodrigues, J. P. P. Gomes, F. T. Brito, I. C. Chaves, M. R. P. Paula, M. R. Salvador, and J. C. Machado, “A fault detection method for hard disk drives based on mixture of gaussians and nonparametric statistics,” IEEE Transactions on Industrial Informatics, vol. 13, no. 2, pp. 542–550, 2017.
J. P. Liu, O. F. Beyca, P. K. Rao, Z. J. Kong, and S. T. Bukkapatnam, “Dirichlet process gaussian mixture models for real-time monitoring and their application to chemical mechanical planarization,” IEEE Transactions on Automation Science and Engineering, vol. 14, no. 1, pp. 208–221, 2017.
K. B. Johnston and A. M. Peter, “Variable star signature classification using slotted symbolic markov modeling,” New Astronomy, vol. 50, pp. 1–11, 2017.

## Slide 5
Limitations - Existing EIDS
  Offline learning and Laborious process of supervised learning
    Collect measurements and logs
    Label measurements and logs
    Train machine learning model on labeled data
    Deploy the trained model to the device
    Execute the model on observed measurements
  High processing cost
  Low accuracy
research motivation
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 6
Challenges
  Destructive-stealthy patterns Data collection and communication in power transmission control systems are subjected to contaminate with destructive-stealthy-data pattern
    Attacker – monitor normal system and mix up payload to camouflage abnormal behavior
    High similarity b/w natural events and malicious-intentional physical faults
    High similarity b/w legitimate and illegal command and control artifacts
  Variety, Velocity and volume (3Vs) PMUs, the major component of the system produce the data at 120 measurements of 28 x quantities
    A dataframe of size [120 x 28] per PMU
research motivation cont.

## Slide 7
Validity - Challenges and Limitations
  Using literature, analytical and empirical analysis by considering prevalent ML Algorithms and available power system dataset of ORNL and Mississippi State University
research motivation cont.

## Slide 8
A flare, is a type of firework that produces a brilliant light and is used for signaling, illumination, or defensive countermeasures in civilian and military.
So too, Flare is a lightweight EIDS, capable of signaling the anomalies, to take defensive countermeasures.
Flare Overview
  Plug and play
  Very Low processing cost (Can be deployed on Raspberry Pi )
  Online learning – (Opposed to offline)
  learn without supervision
  Improved accuracy
  Open Source (Code will be available at github after approvals)

## Slide 9
Alert
Flare Overview cont.
Flare
Flare can be deployed at:
  Substation – A Dedicated server or SBC
  Central Control Center – A Dedicated Server

## Slide 10
Relay
Phasor measurement unit
28 x Measurements
Current
Voltage
Magnitude
Impedance
Frequency
snort
Snort Log
TRUE
FALSE
Relay Status
TRUE
FALSE
control room
Control Room SW Log
TRUE
FALSE
Alert
Flare Overview cont.

## Slide 11
Gaussian mixture model (GMM) and Correntropy
  Promising results by GMM and Correntropy approaches reported in literature [1], [2], [3], [4] and [5]
    Their use in the Electrical Power system event and intrusion detection domain is novel.
  GMM allows us to aggregate a multivariate data sequences of power transmission control system into one variable to have numeric behavioral representation for decision making
  Correntropy measure is operated on the posterior probabilities of the GMM to accurately establish the baseline for the normal system and detect anomalies.
Flare Overview cont.
Notes: Waqas Haider, PHD research work “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, 2018, The University of New South Wales
A. Lagrange, M. Fauvel, and M. Grizonnet, “Large-scale feature selection with gaussian mixture models for the classification of high dimensional remote sensing images,” IEEE Transactions on Computational Imaging, vol. 3, no. 2, pp. 230–242, 2017.
L. P. Queiroz, F. C. M. Rodrigues, J. P. P. Gomes, F. T. Brito, I. C. Chaves, M. R. P. Paula, M. R. Salvador, and J. C. Machado, “A fault detection method for hard disk drives based on mixture of gaussians and nonparametric statistics,” IEEE Transactions on Industrial Informatics, vol. 13, no. 2, pp. 542–550, 2017.
J. P. Liu, O. F. Beyca, P. K. Rao, Z. J. Kong, and S. T. Bukkapatnam, “Dirichlet process gaussian mixture models for real-time monitoring and their application to chemical mechanical planarization,” IEEE Transactions on Automation Science and Engineering, vol. 14, no. 1, pp. 208–221, 2017.
K. B. Johnston and A. M. Peter, “Variable star signature classification using slotted symbolic markov modeling,” New Astronomy, vol. 50, pp. 1–11, 2017.

## Slide 12
Gaussian mixture model (GMM) and Correntropy
  Malicious-stealthy-data patterns and legitimate event data dynamics are errors from decision making point of view
  These errors create an element of bias in data sequences
  Effect of this bias may be very large, it cannot be overlooked or treated as minor noise (non-gaussian or impulsive)
  To process non-Gaussian and impulsive noises [waqas 51], the notion of Correntropy, which is a local measure of the similarity between any two random variables, is suggested in [waqs52]
  Correntropy measure the precise behavioral boundaries for decision purposes.
    Posterior probabilities (are utilized) of the data sequences obtained from GMM as input to the Correntropy as suggested in [1].
    Because the interdependency of the power system’s data sequences can be more reliably estimated based on their prior and likelihood data distributions, i.e., posterior = prior x likelihood.
Introduction
Notes: Waqas Haider, PHD research work “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, 2018, The University of New South Wales
A. Lagrange, M. Fauvel, and M. Grizonnet, “Large-scale feature selection with gaussian mixture models for the classification of high dimensional remote sensing images,” IEEE Transactions on Computational Imaging, vol. 3, no. 2, pp. 230–242, 2017.
L. P. Queiroz, F. C. M. Rodrigues, J. P. P. Gomes, F. T. Brito, I. C. Chaves, M. R. P. Paula, M. R. Salvador, and J. C. Machado, “A fault detection method for hard disk drives based on mixture of gaussians and nonparametric statistics,” IEEE Transactions on Industrial Informatics, vol. 13, no. 2, pp. 542–550, 2017.
J. P. Liu, O. F. Beyca, P. K. Rao, Z. J. Kong, and S. T. Bukkapatnam, “Dirichlet process gaussian mixture models for real-time monitoring and their application to chemical mechanical planarization,” IEEE Transactions on Automation Science and Engineering, vol. 14, no. 1, pp. 208–221, 2017.
K. B. Johnston and A. M. Peter, “Variable star signature classification using slotted symbolic markov modeling,” New Astronomy, vol. 50, pp. 1–11, 2017.

## Slide 13
  Why GMM and Correntropy (Corr-GMM) is used to model Detection engine
  Power transmission control system data normal data is highly dynamic and multi dim (28)
  Malicious-stealthy-data patterns and legitimate event data dynamics are errors from decision making point of view
  These errors create an element of bias in data sequences
  Effect of this bias may be very large, it cannot be overlooked or treated as minor noise (non-gaussian or impulsive)
  To process non-Gaussian and impulsive noises [waqas 51], the notion of Correntropy, which is a local measure of the similarity between any two random variables, is suggested in [waqs52]
Introduction
Notes: Waqas Haider, PHD research work “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, 2018, The University of New South Wales
A. Lagrange, M. Fauvel, and M. Grizonnet, “Large-scale feature selection with gaussian mixture models for the classification of high dimensional remote sensing images,” IEEE Transactions on Computational Imaging, vol. 3, no. 2, pp. 230–242, 2017.
L. P. Queiroz, F. C. M. Rodrigues, J. P. P. Gomes, F. T. Brito, I. C. Chaves, M. R. P. Paula, M. R. Salvador, and J. C. Machado, “A fault detection method for hard disk drives based on mixture of gaussians and nonparametric statistics,” IEEE Transactions on Industrial Informatics, vol. 13, no. 2, pp. 542–550, 2017.
J. P. Liu, O. F. Beyca, P. K. Rao, Z. J. Kong, and S. T. Bukkapatnam, “Dirichlet process gaussian mixture models for real-time monitoring and their application to chemical mechanical planarization,” IEEE Transactions on Automation Science and Engineering, vol. 14, no. 1, pp. 208–221, 2017.
K. B. Johnston and A. M. Peter, “Variable star signature classification using slotted symbolic markov modeling,” New Astronomy, vol. 50, pp. 1–11, 2017.

## Slide 14
Power Line faults and contingencies
Power Line Faults
Notes: Waqas Haider , “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, UNSW, 2018

## Slide 15
Line Maintenance
Power Line faults and contingencies
Notes: Waqas Haider , “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, UNSW, 2018

## Slide 16
Cyber Attack on Power System
Data Injection Attack
Notes: Waqas Haider , “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, UNSW, 2018

## Slide 17
Cyber Attack on Power System
Command Attack
Notes: Waqas Haider , “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, UNSW, 2018

## Slide 18
Cyber Attack on Power System
Relay Setting Attack
Notes: Waqas Haider , “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, UNSW, 2018

## Slide 19
Flare system design
Synchrophasor measurements
Data Logs from,
  Snort
  Control panel
  Relays
Gaussain Probability
density
estimation
Event Parsor
And
Processer
1
1
2
2
3
CorrEntroy
3
4
CorrEntroy
Detector Threshold
4

## Slide 20
Central Limit Theorem
  "If the mean of a random sample of size drawn from a population with mean and variance , the sampling distribution of approaches the gaussian distribution with mean and variance σ /n as the sample size n increases without limit“
  Histograms of sampling means of power system WAMS’s quantities, voltage and current synchrophasors tends to be normally distributed / gaussian.

## Slide 21
Central Limit Theorem
*Plots created in Minitab V18

## Slide 22
  How and why GMM and Correntropy (Corr-GMM) is used
  Malicious-stealthy-data patterns and legitimate event data dynamics can be viewed as errors in statistics
  These errors can play a vital role from decision engine point of view
  Errors create an element of bias in data sequences
  Effect of this bias cannot be overlooked or treated as minor noise (non-gaussian or impulsive)
  To process non-Gaussian and impulsive noises the notion of Correntropy, which is a local measure of the similarity between any two random variables, is suggested in [Haider, PHD Thesis]
Flare system design
Notes: Waqas Haider , “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, UNSW, 2018

## Slide 23
  How and why GMM and Correntropy (Corr-GMM) is used
  Correntropy measure is used to create the precise behavioral boundaries for classification purposes.
  We utilized the posterior probabilities of the data sequences obtained from GMM as input to the Correntropy as suggested in [Haider, PHD Thesis] Because the interdependency of the power system’s data sequences can be more reliably estimated based on their prior and likelihood data distributions, i.e., posterior = prior x likelihood.
Flare system design cont.
Notes: Waqas Haider , “Developing Reliable Anomaly Detection System for Critical Hosts: A Proactive Defense Paradigm”, UNSW, 2018

## Slide 24
Alert
Flare Framework cont.
Symbol | Description
 | A multi-dimensional random variable, ; where m is the number of features
 | Feature variable;
 | Mean of observations of jth feature
 | Standard Deviation of observations of jth feature
 | Probabilistic proportions/ weight of each feature
and | 3.14159 and 2.71828
 | Gaussian/ Normal Distribution
Symbol | Description
 | Mean of observations of jth feature
 | Standard Deviation of observations of jth feature
 | Probabilistic proportions/ weight of each feature
 | 3.14159 and 2.71828
 | Gaussian/ Normal Distribution
important notations to proceed in-depth understanding of Flare working mechanism

## Slide 25
FLARE FRAMEWORK cont.
π = 3.14159
e = 2.71828
I = {xi1,…xij,…xim}
Each feature variable (i.e. PMU’s quantities) comprise n measurements, where the ith reading from the m-dimensional
X variable space is expressed as,
Each feature variable can be modeled gaussian distribution (GD) and probability density function is estimated
Eq 1

## Slide 26
FLARE FRAMEWORK cont.
The posterior probability of taking the ith measurement value (Xi)
formulated by,
The posterior probabilities of all the whole measurements can be
estimated by,
Eq 2
Eq 3

## Slide 27
The Correntropy of the two consecutive observations,
FLARE FRAMEWORK cont.
The Correntropy of the two consecutive observations,
| )
Correntropy-induced metric (CIM) employed by (Haider, 2018) to measure the local similarity between to measurements, for any two observations (A and B) is as:
Upper and Lower correntropy values are used to accurately specify a normal proﬁle,
Eq 4
Eq 5
Eq 6

## Slide 28
FLARE FRAMEWORK cont.
Input
i for sequences and k for features) | k=1 | k=2 | k=3 | k=4 | Label
i=1 | 1 | 2 | 3 | 4 | Normal
i=2 | 2 | 3 | 4 | 5 | Normal
i=3 | 3 | 4 | 5 | 6 | Normal
i=4 | 4 | 5 | 6 | 7 | Normal
i=5 | 5 | 6 | 7 | 8 | Normal
i=6 | 6 | 7 | 8 | 9 | Normal
Mean (µ) | 3.5 | 4.5 | 5.5 | 6.5
Standard deviation (σ) | 1.870828693 | 1.870828693 | 1.870828693 | 1.8708286
Variance ( ) | 3.5 | 3.5 | 3.5 | 3.5
Weight (𝜔) | 0.25 | 0.25 | 0.25 | 0.25
Parameters Estimation
Flare during Learning

## Slide 29
FLARE FRAMEWORK cont.
Probability Density Function (PDF) estimation
Flare during Learning
0.087319877 | 0.087319877 | 0.087319877 | 0.087319877
0.154625597 | 0.154625597 | 0.154625597 | 0.154625597
0.205762168 | 0.205762168 | 0.205762168 | 0.205762168
0.205762168 | 0.205762168 | 0.205762168 | 0.205762168
0.154625597 | 0.154625597 | 0.154625597 | 0.154625597
0.058951848 | 0.120422536 | 0.18485618 | 0.213243619
0.021829969 | 0.021829969 | 0.021829969 | 0.021829969
0.038656399 | 0.038656399 | 0.038656399 | 0.038656399
0.051440542 | 0.051440542 | 0.051440542 | 0.051440542
0.051440542 | 0.051440542 | 0.051440542 | 0.051440542
0.038656399 | 0.038656399 | 0.038656399 | 0.038656399
0.014737962 | 0.030105634 | 0.046214045 | 0.053310905
PDF with weights
0.087319877
0.154625597
0.205762168
0.205762168
0.154625597
0.144368546
Posterior
using Eq 1
using Eq 2
using Eq 3

## Slide 30
FLARE FRAMEWORK CONT
Calculate correntropies
Flare during Learning
Calculate the upper correntropy and lower correntropy using
equation 5 and 6.
using Eq 4
1.000007444
1.000008769
1.000008944
1.000007444
1.000005945
1.000007195
Lower corr normal | 1.000005945
Upper corr normal | 1.000008944

## Slide 31
FLARE FRAMEWORK cont.
Estimate the PDFs using the parameters of normal profile and
Calculate the correntropies using equations mentioned before.
Flare during Execution
Compare the correntropies against the decision correntropies
using,

## Slide 32
  Why GMM and Correntropy (Corr-GMM) is used to model Detection engine
  Data collection and transmission over power system are subjected to contaminate with destructive-stealthy-data pattern
  While logging Power system then logged data is multi model data/ multi dim (28)
  Power system’s normal data is highly dynamic due to number and purposes of stakeholders (i.e., consumers and managers).
  Malicious-stealthy-data patterns and legitimate event data dynamics are errors from decision making point of view
  These errors create an element of bias in data sequences
  Effect of this bias may be very large, it cannot be overlooked or treated as minor noise (non-gaussian or impulsive)
  To process non-Gaussian and impulsive noises [waqas 51], the notion of Correntropy, which is a local measure of the similarity between any two random variables, is suggested in [waqs52]
RATIONALE OF UTILZED MATH MODEL
The data patterns become stealthy due to: a) attacker’s monitoring of system behaviour and mixing malicious payload to camouflage abnormal behaviour b) high similarity between natural and malicious-intentional physical faults; and c) high similarity between legitimate and illegal command and control artefacts.

## Slide 33
  Why GMM and Correntropy (Corr-GMM) is used to model Detection engine Cont.
  Correntropy measure the precise behavioral boundaries for classification purposes.
  Utilized the posterior probabilities of the data sequences obtained from GMM as input to the Correntropy as suggested in [1]. Because the interdependency of the power system’s data sequences can be more reliably estimated based on their prior and likelihood data distributions, i.e., posterior = prior x likelihood.
  GMM also allows to aggregate a multivariate data sequence of power sys into one variable to have numeric behavioral representation for decision making
  GMM and Correntropy approaches have been successfully implemented in a number of applications, including recognition [15], [16], [17], [18], their use in the Power system EIDS domain is novel.
RATIONALE OF UTILZED MATH MODEL

## Slide 34
results
  Flare Performance Evaluation
    To evaluate the performance of Flare, we performed benchmarks,
      On a Raspberry Pi 3 Model B, 1.2 GHz and 1GB RAM (Substation Depl)
      A Windows 10 running on an Intel Core i7 CPU 870, 2.93 GHz with 8GM (Central Depl)
    Complete implementation is done in Python.
The DR, FAR represents the accurac and error of Flare, respectively. The
FAR is the average of two errors, the False Positive Rate (FPR) and False
Negative Rate (FNR).
FAR can well indicate the capacity of Flare to incorrectly detect normal behavior as abnormal and abnormal behavior as normal, respectively (Haider, 2018).
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 35
results – Central Deployment
Scenario | FPrate | FNrate | Error Rate | DRate
Attack vs. Normal | 3.0328 | 4.603 | 3.818 | 95.39745835
Data Injection vs. Normal | 7.8204 | 0.714 | 4.267 | 99.28634168
Line Maintenance vs. Normal | 7.8204 | 1.398 | 4.609 | 98.60228717
Fault Events vs. Normal | 7.8204 | 0.714 | 4.267 | 99.2857643
Command Injection vs. Norma | 7.8204 | 2.291 | 5.056 | 97.7092828
Relay Setting Change vs. Normal | 7.8204 | 4.909 | 6.365 | 95.09097435
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 36
results – Substation - IED Deployment
Scenario | FPrate | Fnrate | Errorrate | Drate
Command Injection | 0 | 1.513877208 | 0.75694 | 98.486
Data Injection | 9.2 | 4.6 | 0.75694 | 90.79
SLG Fault | 0 | 3.25 | 1.62 | 96.74
Line Maint | 0 | 3.25 | 1.62 | 96.74
Relay Setting Change | 0 | 9.2 | 4.6 | 90.72
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 37
results – datasets for Cen Depl
Attacks Name | Description | # of measurements | Train [sec] | Execute [sec]
Data Injection | Imitation of a valid fault by changing values to parameters such as current, voltage, sequence components etc. This attack aims to blind the operator and causes a black out. | Train = 2423 Execute = 11564 | 22 | 100
Command injection - Remote trip relay | Attacker sends a command to a relay which causes a breaker to open. It can only be done once an attacker has penetrated outside defenses | Train = 2423 Execute = 10719 | 21 | 93
Event Name | Description | # of measurements | Train [sec] | Execute [sec]
Short-circuit fault | This is a short in a power line and can occur in various locations along the line. | Train = 2423 Execute = 16982 | 21 | 93
Line Maintenance | Relays is disabled on a specific line to do maintenance for that line | Train = 2423 Execute = 5291 | 22 | 46
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 38
Scenario | Description | # of measurements | Train [sec] | Execute [sec]
Command injection - Relay setting change | Relays are configured with a distance protection scheme and the attacker changes the setting to disable the relay function such that relay will not trip for a valid fault or a valid command. | Train = 2423 Execute = 39326 | 21 | 364
Anomaly | The training dataset is composed o f the measurements from normal, natural faults and line maintenance and test dataset composed of | Train = 12490 Execute = 65889 | 115 | 639
results – datasets for Cen Depl
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 39
results – datasets for Substation Depl
Scenario | # of measurements | Train [sec] | Execute [sec]
Short-circuit fault | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 14243 | 43 | 137
Line Maintenance | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 3041 | 43 | 127
Data Injection | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 9582 | 43 | 192
Command injection - Remote trip relay | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 8739 | 43 | 44
Command injection - Relay setting change | Nomral Training Instance = 3524 Normal Test Instance = 879 Attack Test Instance = 36159 | 43 | 142
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 40
Comparison
Algorithm(s) | Result
Naïve Bayes,OneR, NNge, Jripper,Random Forests,SVM,Adaboost | JRipper+Adaboost having the highest overall F-Measure 0.955
Novel Specification-based Bayesian network | 100% for Nine scenarios
Sequential Pattern Mining algorithm | 95 % for Experiment 1 87.6% fro Experiment 2 93.21 % for Experiment 3
Temporal state-based specifications Learning | 90.4 % accuracy 73.43 % For Zero-days
Fuzzy c-means (FCM) algorithm combined with the fuzzy inference system (FIS) | 99.11 % Overall accuracy
Hoeffding Adaptive Trees (HAT) augmented with the drift detection method (DDM) and adaptive windowing (ADWIN) | The average kappa statistic was 94% for binary and 93% for multiclass classification.
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 41
Algorithm(s) | Result
Specification-Based and Decision trees, instance-based learning and NNGE | NNGE+STEM algorithm provides 96% and 93% detection accuracy for Binary and Multi Class datasets HAT algorithm provides 98% and 92% for Binary and Multi Class datasets respectively
Non mested generalized Exampler (NNGE) with State Extraction Method (STEM) | 94.0% with NNGE for Multiclass Classification 98% with NNGE for Binary Class Classification 99.54% with NNGE for Multi Class Classification on the IEEE 9 Bus System
Extreme Learning Machine (ELM) model optimized by the Adaptive Elitist Differential Evolution algorithm (AEDE) | 96.55% with proposed AEDE-ELM
Comparison
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 42
Algorithm(s) | Result
Stacked Sutoencoders | 99.89 % for Normal Events 98.94 % for Data Injection Attacks 97.34% for Command Injection Attack 98.53 % for Relay Setting Change Attack
Probabilistic classification (Bayesnet), Rule induction (OneR, Ripper), Decision tree learning (C4.5), Non-probabilistic binary classification (SVM), The Ensemble Methods (Adaptive boosting, Bagging, Majority voting, Random forest) | Bagging C4.5, Adaboost Ripper, Adaboost C4.5 and Random forest achieved more than 90 % accuracy
NNGE HAT Common Path Mining | 94 % with NNGE 94% with HAT 93% with Common Path Minng Algoithm
Comparison
Notes: Uttam Adhikari, “Event and intrusion detection systems for cyber-physical power systems”, Ph.D. dissertation, Mississippi State University, August 2015.
Pan, Shengyi, Thomas H. Morris, and Uttam Adhikari. "A Specification-based Intrusion Detection Framework for Cyber-physical Environment in Electric Power System." IJ Network Security 17, no. 2(2015): 174-188.

## Slide 43: Thank You